## Slide 1
⚡
FAULT
CCR
1001
1015
1030
1045
1060
1075
1085
1090
Team 5
Earth Fault Detection
Physics-guided spatial fault localization using PLC telemetry
90-fixture series circuit · 3 test runs · Ranked fault zones with confidence
Sadia Parveen
Apu Bhowmick
Truc Do
Luis Herrera P.

## Slide 2
PHYSICS INSIGHT
Earth Faults Leak Communication
Signal — Not Only Power
CCR
⚡
signal leaks
to ground
Upstream: healthy signal
Downstream: weaker, noisier comms
Observable symptoms along the 90-fixture chain:
Response Rate
drops near fault
Repeater Depth
increases beyond fault
📡
Phase Noise
rises around fault
⚡
CRC / BER
errors cluster spatially

## Slide 3
OUR METHOD
Spatial Anomaly Localization
Across the Fixture Chain
1
Parse CSV
Split into COMM
RATES · EXCOMM
CORR families
2
Aggregate
One feature row
per fixture across
all message types
3
Baseline
Normalize
Compare each
fixture to its
no-fault baseline
4
Score &
Smooth
Anomaly score
per fixture ·
Smoothed spatially
5
Rank
Zones
Top candidate
regions + change-
points detected
Core Idea
Not a classifier. We build a spatial anomaly profile across the ordered 90-fixture chain and look for spatial change-points, degradation steps, or clustered anomalies that reveal where the fault sits — explainably and without needing labels.
Spatial Patterns We Look For
Step / Change-Point
Sharp transition between healthy upstream and degraded downstream fixtures.
Gradient / Slope
Gradual roll-off of signal quality across a span — soft or high-impedance fault.
Clustered Degradation
Bounded group of adjacent fixtures departing together from baseline.

## Slide 4
SCORING DETAIL
How the Anomaly Score Is Built
1
No-fault Baseline
Per fixture + feature: baseline mean & std dev
2
Z-score
z = (value − mean) / std
3
Direction-Aware Score
High-is-worse: max(0, z) Low-is-worse: max(0, −z) Cap at 5
4
Family Scores
COMM · RATES · EXCOMM · CORR
5
Fixture Anomaly Profile
Combine family scores · order 1001 → 1090
6
Zone Score
Smooth across neighbors · find high-scoring contiguous regions
7
Confidence
Anomaly strength + spatial sharpness + family agreement
From raw telemetry to ranked zone
Per-fixture · Per-feature
z = (value − mean) / std
max(0, ±z) capped at 5
COMM
RATES
EXCOMM
CORR
4 independent family scores
Fixture anomaly profile
1001 ──────────────── 1090
Confidence
Anomaly strength
How far above baseline?
Spatial sharpness
Sharp step vs soft gradient
Family agreement
Do COMM, RATES, EXCOMM, CORR agree?
Temporal consistency
Stable across 15-min window?
Output:
HIGH
MEDIUM
LOW
UNCERTAIN
SCORING DETAIL
How the Anomaly Score Is Built
1
No-fault Baseline
Per fixture + feature: baseline mean & std dev
2
Z-score
z = (value − mean) / std
3
Direction-Aware Score
High-is-worse: max(0, z) Low-is-worse: max(0, −z) Cap at 5
4
Family Scores
COMM · RATES · EXCOMM · CORR
5
Fixture Anomaly Profile
Combine family scores · order 1001 → 1090
6
Zone Score
Smooth across neighbors · find high-scoring contiguous regions
7
Confidence
Anomaly strength + spatial sharpness + family agreement
From raw telemetry to ranked zone
Per-fixture · Per-feature
z = (value − mean) / std
max(0, ±z) capped at 5
COMM
RATES
EXCOMM
CORR
4 independent family scores
Fixture anomaly profile
1001 ──────────────── 1090
Confidence
Anomaly strength
How far above baseline?
Spatial sharpness
Sharp step vs soft gradient
Family agreement
Do COMM, RATES, EXCOMM, CORR agree?
Temporal consistency
Stable across 15-min window?
Output:
HIGH
MEDIUM
LOW
UNCERTAIN

## Slide 5
PROTOTYPE RESULTS
Example Output: Fixtures 1064–1086
Example Prediction
MEDIUM
Top zone: 1064–1086
Anomaly Score: 1.6362
Message type contribution
contributing
Evidence
rxCrcFailCount elevated
berCount rising ~1060+
EXCOMM + CORR align
Gradient rise visible

## Slide 6
PROTOTYPE RESULTS
Conservative but Explainable
Fault-Zone Ranking
80
Scenarios
processed
7,200
Fixture-level rows
created
12/12
No-fault scenarios
correctly Uncertain
Confidence Distribution — Faulted Scenarios
Uncertain
20
Low confidence
50
Medium confidence
10
Total faulted scenarios: 68 (80 total − 12 no-fault baselines)
Interpretation
Safe by design
Model refuses to hallucinate a zone. "Uncertain" is the honest answer when signal is weak.
Physical-layer driven
EXCOMM/CORR (CRC failures, BER, SNR) carry the strongest fault fingerprint.
Conservative, not wrong
High-impedance faults (30–50 kΩ) produce faint signals — wider zones or Uncertain are correct.
No-fault: 100% correct
All 12 baseline scenarios correctly returned no localized zone.

## Slide 7
Actual Prediction

## Slide 8
RECOMMENDATION
Recommendation: 3-Step Pipeline
Anomaly Detection
→
Feature Engineering
→
Classification
1
Anomaly Detection
Is there a fault?
INPUT
→ Raw CSV (15 min telemetry)
→ Baseline (loc=0) reference
LOGIC
Compute BER delta per fixture
SNR = max(BER_delta) / noise_floor
Compare against threshold tiers
OUTPUT
✓ NONE → stop, cannot localize
✓ LOW / MEDIUM / HIGH → proceed
2
Feature Engineering
What does the pattern look like?
INPUT
→ 90 fixture × raw metrics
LOGIC
Subtract baseline per fixture
Z-score, gradient, rolling mean
Flatten to spatial signature vector
OUTPUT
✓ 810-feature vector
✓ 90 fixtures × 9 spatial metrics
3
Classification
Which location (1–4)?
INPUT
→ 810-feature spatial vector
→ Trained Random Forest (200 trees)
LOGIC
predict_proba → 4 class scores
Rank locations by probability
Attach confidence tier from Step 1
OUTPUT
✓ Ranked list: loc2 68%, loc3 20%...
✓ Confidence: HIGH / MEDIUM / LOW